DB2 Stop/Start Procedure with TSA

NOTE : Run lssam command on both primary and Standby as a1insctp user and make a note → Once recycle completed, we compare the results.

Run below command on rdb025 as root:

        export CT_MANAGEMENT_SCOPE=2
        chrsrc -c IBM.PeerNode CritRsrcProtMethod=5

2 . Disable TSA, Login as a1insctp on rdb025 and rdb024:

        Sequence is Prime then Standby DB Servers.

      Prime database as a1insctp:

  As DB2 instance owner on BOTH nodes (primary first)	db2haicu -disable
  when prompted if you want to stop, select option for Yes (just press "1" then ENTER)

(A)a1insctp@g01cxcp20058:/home/a1insctp#db2haicu -disable

Welcome to the DB2 High Availability Instance Configuration Utility (db2haicu).

      Are you sure you want to disable high availability (HA) for the database instance 'a1insctp'. This will lock all the resource groups for the instance and disable the HA configuration parameter. The instance will not failover if a system outage occurs while the instance is disabled. You will need to run db2haicu again to enable the instance for HA. Disable HA for the instance 'a1insctp'? [1]
1. Yes
2. No
1 -----------> Select '1'
Disabling high availability for instance 'a1insctp' ...
Disabling high availability for instance 'a1insctp' was successful.
All cluster configurations have been completed successfully. db2haicu exiting ...
a1insctp@g01cxcp21056:/home/a1insctp#

       Standby database as a1insctp:

a1insctp@g01cxcp21056:/home/a1insctp#db2haicu -disable
Welcome to the DB2 High Availability Instance Configuration Utility (db2haicu).

      Are you sure you want to disable high availability (HA) for the database instance 'a1insctp'. This will lock all the resource groups for the instance and disable the HA configuration parameter. The instance will not failover if a system outage occurs while the instance is disabled. You will need to run db2haicu again to enable the instance for HA. Disable HA for the instance 'a1insctp'? [1]
1. Yes
2. No
1 -----> Select '1'
Disabling high availability for instance 'a1insctp' ...
Disabling high availability for instance 'a1insctp' was successful.
All cluster configurations have been completed successfully. db2haicu exiting ...
a1insctp@g01cxcp21056:/home/a1insctp#

Deactivate the database on both Primary and Standby:
        On Primary(025) db:
        db2 terminate
        db2 force application all
        db2 connect to saleconn
        db2 quiesce db immediate force connections
        db2 terminate
        db2 deactivate db saleconn
 db2 stop hadr on db saleconn
        On Standby(024) db:
        db2 terminate
        db2 force applications all
        db2 list applications
        db2 deactivate db saleconn
 db2 stop hadr on db saleconn
Stop the db2 instance on both Primary and Standby (Primary first):
        db2stop force
        Check the process using: ps -ef | grep db2sysc | grep -v grep

 ***NOTE: If we have any AIX reboot, wait till its done by AIX team. This is not always necessary***

Start the db2 on Standby server(024):
        db2start
        db2 activate db saleconn

6. Start db2 on Prime server(025):

        db2start
        NOTE: wait until HADR comes peer State before activating db on primary.
        db2 activate db saleconn

        NOTE: If activate fails on Standby/Primary then only do the following:
        On standby db (024) :	db2 start hadr on db saleconn as standby
        On Prime db(025) :	db2 start hadr on db saleconn as primary

        NOTE: Before starting TSA make sure that the following shows on both primary/standby
        db2pd -d saleconn -hadr status|grep STATE
  HADR_STATE = PEER
        HADR_CONNECT_STATUS = CONNECTED

7. Re-enable TSA:

    On Standby(024) server as a1insctp:

a1insctp@g01cxcp21056:/home/a1insctp#db2haicu

        db2haicu has detected that high availability has been disabled for the instance 'a1insctp'. Do you want to enable high availability for the instance 'a1insctp'? [1]
1. Yes
2. No
1 ----> Select '1'
        The following are valid settings for the high availability configuration parameter:
  1.TSA
  2.Vendor
Enter a value for the high availability configuration parameter: [1]
1 ----> Select '1'

    On Prime server(025) as a1insctp:

a1insctp@g01cxcp20058:/home/a1insctp#db2haicu

        db2haicu has detected that high availability has been disabled for the instance 'a1insctp'. Do you want to enable high availability for the instance 'a1insctp'? [1]
1. Yes
2. No
1 ----> Select '1'
        The following are valid settings for the high availability configuration parameter:
  1.TSA
  2.Vendor
Enter a value for the high availability configuration parameter: [1]
1 ----> Select '1'

8. Change chrsrc parameter as root on both Primary and Standby (as root):

        As root ( On Prime and Standby): chrsrc -c IBM.PeerNode CritRsrcProtMethod=3

Verify the Cluster with below command ( Primary/Standby):
lssam
        NOTE: Result should match with the one we took before recycle.

        -----------END OF THE DOCUMENT-----------